## Slide 1
RCAR GEN3 CONFORMAL ECO
  Subline
Date : Dec.08.2018
Name : AnNGuyen
Renesas Electronics Corporation

## Slide 2: Agenda
RCAR Gen3 Conformal ECO Flow
RCAR Gen3 Conformal ECO Issue

## Slide 3: RCAR GeN3 Conformal ECO FLOW
RTL 1
module_netlist 1
Hier_preDFT
Hier_postISO
Hier_postJTAG
Hier_postLAY
synthesis
DFT insertion
ISO insertion
Layout optimization
RTL 2
module_netlist 2
synthesis
Grouping + RLcheck + TMR insert + DFTwrapper
posteco_RTL 2
ECO
synthesis
posteco_netlist
separate
separate
separate
preeco_postISO_netlist
preeco_postJTAG_netlist
preeco_postLAY_netlist
Hier_postDFT
JTAG insertion
separate
preeco_postDFT_netlist
Conformal ECO
posteco_postDFT_netlist
Conformal ECO
posteco_postISO_netlist
posteco_postJTAG_netlist
Conformal ECO
Conformal ECO
posteco_postLAY_netlist
preeco : before eco
posteco : after eco
posteco_postLAY_CMD
posteco_postJTAG_CMD
posteco_postISO_CMD
posteco_postDFT_CMD

## Slide 4: RCAR GeN3 Conformal ECO ISSUE (1/2)
posteco_RTL
synthesis
posteco_netlist
preeco_postISO_netlist
preeco_postJTAG_netlist
preeco_postLAY_netlist
preeco_postDFT_netlist
Conformal ECO
posteco_postDFT_netlist
Conformal ECO
posteco_postISO_netlist
posteco_postJTAG_netlist
Conformal ECO
Conformal ECO
posteco_postLAY_netlist
Issue1
Issue2
Issue3
Issue4
Issue1 : take time to re-synthesis posteco_RTL. In case of V3H DMAC takes about 8hours ( 3hours synthesis + 5hours FM)
Issue2 : need to add setting to cancel DFT circuit. ECO need to add/remove SCANCHAIN.
Issue3 : need to add setting to cancel ISO circuit
Issue4 : need to add setting to cancel JTAG circuit
Issue5 : need to match input port between postJTAG vs postLAY (refer to next slide for more detail).
Issue6 : Conformal ECO modify netlist many points for simple modification.
Issue 7. Unsuccessful ECO generation, Fail FV
Issue5
preeco : before eco
posteco : after eco
Issue7

## Slide 5: Issue1. take time to re-synthesis posteco_RTL. In case of V3H DMAC takes about 8hours ( 3hours synthesis + 5hours FM)
RTL vs Gate ? Not recommendation
Gate vs Gate  recommendation. Take care below
  Same environment to generation Gate
  Coding style
  Conformal-lec may be considered to check equivalence

## Slide 6: Issue 2 ~ 4. Need additional settting
How to get constraint from Hier level to module level?
Read Hier design
Apply constraint at Hier
Use command to write out constraint (refer to material: write_hier_compare_dofile –constraint –MODULE )
Extract constraint at module level

## Slide 7
Issue 5
M1
M2
M1
M2
separate
M1
M2
M1
M2
PreLAY
PostLAY
Added ports in postLAY
Issue5
separate

## Slide 8: Issue 6. Conformal ECO modify netlist many points for simple modification.
Need to replicate issue’
How many noequ point ? Same or much as expectation. If wrong mapping  manual mapping is necessary or using add renaming rule
Logic cone across module boundary. Usually, no sub-module inside one patch.

## Slide 9: Issue 7. Unsuccessful ECO generation
Need to replicate issue
Write out setup in Patch generation (conformal-eco)
Read again in equivalence checking (conformal-lec)  ensure same constraint in setup.
## Or, use formality to confirm equivalent
Nonstop process during patch generation.
Mapping and compare: fast
Analyze (generate patch) long time  change effort level to Medium (default is High)

## Slide 10: Updated version
Conformal-ECO
Gen3: 14.10-s220
V3U-AD : 15.20-s140
What is noticed updated point we need to care ?
Flow is not big difference
Better support for clock tree patch, scan path
18.20* version can overcome scan chain broken issue.

## Slide 11: Communication channel
Webex
Email
On-site support
Via support site

## Slide 13
Renesas.com

## Slide 14: RCAR GeN3 Conformal ECO FLOW
RTL
module_netlist
Hier_preDFT
Hier_postISO
Hier_postJTAG
Hier_postLAY
synthesis
DFT insertion
ISO insertion
Layout optimization
RTL
module_netlist
synthesis
Grouping + Rlcheck + TMR insert
posteco_RTL
ECO
synthesis
posteco_netlist
separate
separate
separate
preeco_postISO_netlist
preeco_postJTAG_netlist
preeco_postLAY_netlist
Hier_postDFT
JTAG insertion
separate
preeco_postDFT_netlist
Conformal ECO
posteco_postDFT_netlist
Conformal ECO
posteco_postISO_netlist
posteco_postJTAG_netlist
Conformal ECO
Conformal ECO
posteco_postLAY_netlist
preeco : before eco
posteco : after eco